## Slide 1
Website for Generating SFD and BMD for Statically Determinate Structures
Introduction
Numerical Analysis
Conclusions
1)Shear Force Diagram (SFD) and Bending Moment Diagram (BMD) are essential tools in structural analysis.
2)They help in understanding internal force variation in beams.
3)Manual calculations are often time-consuming and prone to errors.
4)This project aims to develop a website to automate SFD and BMD generation.
5)The tool enhances visualization and conceptual understanding for students.
Scope
Results and Discussion
1)The website successfully generates accurate SFD and BMD diagrams.
2)Results are consistent with manual calculations.
3)The interface is simple, fast, and efficient.
4)Helps in quick analysis and better understanding of structural behavior.
5)Website can be extended for advanced structural analysis applications, if required.
Professional Association For Civil Engineering, NITK Surathkal
Mentor: Abhijith(231CV152),Vidya(231CV155),Tejas(231CV152) Mentees: Tanmay Sharma(241CV152), Vikash Saini(241CV256)
1)To simplify SFD and BMD calculations for civil engineering students.
2)To provide a user-friendly and interactive web interface.
3)To minimize manual calculation errors.
4)To improve conceptual clarity through visualization.
5)Future scope includes:
  Indeterminate structures
  3D structural analysis
  Real-time simulation
1)Input Parameters:
Beam configuration: Simply Supported / Cantilever
Span length and support conditions
Load cases:
  Point loads
  Uniformly Distributed Loads (UDL)
  Applied moments
2)Support Reaction Calculation:
Reactions are computed using static equilibrium
equations:
  ΣF = 0 (sum of vertical and horizontal forces: Fx,Fy)
  ΣM = 0 (sum of moments about a point)
For multiple loads, superposition is applied. .
1)The developed website effectively performs analysis
of statically determinate beams and generates
accurate SFD and BMD.
2)The tool successfully converts numerical results into
clear graphical representations, improving
visualization of structural behavior.
3)Comparison with manual calculations shows high
accuracy and reliability of the developed system.
4)The project demonstrates how computational tools
can reduce complexity, save time, and minimize
human errors in structural analysis.
5)It serves as an effective learning and teaching aid
for civil engineering students.
6)Future Enhancements:
Extension to statically indeterminate structures
Inclusion of dynamic and moving load analysis
Integration with advanced design modules and 3D
visualization tools
The implementation of equilibrium equations
(ΣF = 0, ΣM = 0) ensures precise computation of
support reactions, shear forces, and bending moments.
3)Shear Force Calculation:
Beam is divided into segments at load application points.
Shear force at any section is calculated by summing vertical forces to the left/right of the section.
Discontinuities are observed at point loads and reactions.
4)Bending Moment Calculation:
Bending moment at a section is obtained by taking moments of forces about that section.
Variation:
  Linear under point loads
  Parabolic under UDL
Maximum bending moment and point of contraflexure are identified.
5)Diagram Generation:
Numerical results are converted into arrays of values along beam length.
Graphs for SFD and BMD are plotted using visualization library (Matplotlib).
Proper scaling and labeling are ensured.